## Slide 1: Command Interpreter

## Slide 2
yes
No
yes
No
Overall Structure
Go to MDSP Error HELP Page
Is ASCII equal to “HELP”?
Print fail message since no function matches the name
Go to Help Function
Print out the prompt and wait for input
When Input Arrives
Is the ASCII Equal to “MDSP”?
yes
Is the Start argument present?
Yes
No
Is the End argument present?
No
Go to First MDSP Function
Store the Start in a Register
Go to Second MDSP Function
Store the start and end arguments in Registers
yes
Go through all function names names in similar fashion
Is ASCII Equal to “EXIT”?
Go to Exit Function
No
This is the last Check all other options are checked at this point
Go Back to Label 1
Label 1

## Slide 3: Debugger commands

## Slide 4
Get Help string and load it to print buffer
Print Help String
Restore the register from main program
Go back to command interpreter
Help

## Slide 5
No
yes
Get start address from interpreter
Convert it from ASCII to HEX
Add $10 to start to get endpoint of the Display
Start =A
Read memory location A
MDSP I
Print ASCII of memory location address
Read contents of Memory Location
Convert Memory Content to ASCII and Print
Is A greater than endpoint?
A = A+1
Go back to command interpreter

## Slide 6
No
yes
Get start and end address from interpreter
Convert start from ASCII to HEX, Start = A
Convert end from ASCII to HEX, End =B
Read memory location A
MDSP II
Print ASCII of memory location address
Read contents of Memory Location
Convert memory content to ASCII and print
Is A greater than B?
A = A+1
Go back to command interpreter

## Slide 7
No
No
No
Get start and end and from interpreter
Convert start from ASCII to HEX, Start = A
Convert end from ASCII to HEX, End =B
Start of sorting algorithm
A=S
SORTW Ascending
S=S+2
Compare S to B
Is S less than B?
Go back to command interpreter
Is (S) less than (S+2)
yes
Swap positions of contents in (S) and (S+2)
Label A
Go back to Label A
Go back to Label B
Label B

## Slide 8
Get start address and size mode from interpreter
Convert start from ASCII to HEX, Start = A
Read memory location A
MM I (for Byte)
Print ASCII of memory location address
Read contents of Memory Location
Convert memory content to ASCII and print
A = A+1
What is size Mode?
Byte
Word, LW
To W or LW MM
Dot(.)
Get User Input
Back to command interpreter
What is user input?
Space
Else
Convert input to Hex
Store it at (A)

## Slide 9
Hex
Get start, data and mode from interpreter
Convert start from ASCII to HEX, Start = A
Data sent in in ASCII =B
Read operation Mode
MS
Convert B from ascii to hex
Store B (hex) in memory location A
Go back to command interpreter
What is Operation mode
ASCII
Store B (ascii) in memory location A

## Slide 10
No
yes
Get start, end and data from interpreter
Convert start from ASCII to HEX, Start = A
Convert end from ASCII to HEX, End =B
Convert data from ASCII to HEX Data=C
BlockFill
Put C in memory location (A)
Is A greater than B?
Go back to command interpreter
A = A+1

## Slide 11
No
yes
Get start, end and move location from interpreter
Convert start from ASCII to HEX, Start = A
Convert end from ASCII to HEX, End =B
Convert move location from ASCII to HEX MoveLoc=C
Blockmove
Put data in A in memory location C
Is A greater than B?
Go back to command interpreter
A = A+1

## Slide 12
No
BlockTest
No
yes
yes
Get start and end from interpreter
Convert start from ASCII to HEX, Start = A
Convert end from ASCII to HEX, End =B
Sample Memory Test Data is C
Put C in memory location (A)
Is A greater than B?
Go back to command interpreter
Is data in A equal to C?
A = A+1
Convert A from Hex to Ascii and print
Convert C from Hex to Ascii and print
Convert Data Read (A) from Hex to Ascii and print

## Slide 13
Yes
BlockSearch
No
No
Get data searched start and end from interpreter
Convert start from ASCII to HEX, Start = A
Convert end from ASCII to HEX, End =B
Convert data searched from ASCII to HEX, Data =C
Is A greater than B?
Go back to command interpreter
Is data in A equal to C?
A = A+1
Convert A from Hex to Ascii and print
Convert C from Hex to Ascii and print
yes
Print Error and go back to command interpreter

## Slide 14
Get destination from command interpreter
Convert destination from ASCII to HEX
Jump to the location
Go

## Slide 15
Print Current Program counter
Print current status register
Print SSP
Print USP
DF
Load Registers from Stack
Store Registers used for printing in memory
Print D0 through D7
Print A0 through A6
Restore Registers and Go back to command interpreter

## Slide 16
Convert Hex to Ascii or Ascii to Hex
ASCII
Hex
Get data and mode from interpreter
Interpreter Data = A
Print first digit as Integer
Go back to command interpreter
What is Operation mode
Display Data from Interpreter using Trap
Convert A to HEX using subroutine
Print second digit as integer

## Slide 17
Clear Registers
Move registers used for printing to stack
Set A0 through A6 to 0
Set D0 through D7 to 0
Print message showing registers are cleared
Go Back to Command Interpreter

## Slide 18
Get destination from command interpreter
Convert destination from ASCII to HEX
Jump to the location
Go

## Slide 19
Exit

## Slide 20: Exception Handlers

## Slide 21
Print Bus Error Text
Get Bus Address from Stack adding 18
Print BA label and the BA from prev. step
Get IR From Stack by adding 22
Bus Error
Restore Registers
Go to DF and print registers there
Print IR label and the IR from prev. step
Get SSW from Stack adding 16
Print SSW label and the SSW from prev. step

## Slide 22
Print Address Error Text
Get Bus Address from Stack adding 18
Print BA label and the BA from prev. step
Get IR From Stack by adding 22
Address Error
Restore Registers
Go to DF and print registers there
Print IR label and the IR from prev. step
Get SSW from Stack adding 16
Print SSW label and the SSW from prev. step

## Slide 23
Print Illegal Instruction Text
Get Bus Address from Stack adding 18
Print BA label and the BA from prev. step
Illegal Instr Error
Go to DF and print registers there

## Slide 24
Print Privelege violation Text
Get Bus Address from Stack adding 18
Print BA label and the BA from prev. step
Privilege Violation Error
Go to DF and print registers there

## Slide 25
Print Divide by Zero Text
Get Bus Address from Stack adding 18
Print BA label and the BA from prev. step
Divide by Zero Error
Go to DF and print registers there

## Slide 26
Print Check Instruction Text
Get Bus Address from Stack adding 18
Print BA label and the BA from prev. step
Check instruction
Go to DF and print registers there

## Slide 27
Print Line A or Line F Exception Text
Get Bus Address from Stack adding 18
Print BA label and the BA from prev. step
Check instruction
Go to DF and print registers there

## Slide 28: EXTRA Stuff
PUT HEX TO ASCII AND ASCII TO HEX HERE

## Slide 29
Does Command Match G
Print BA label and the BA from prev. step
Overall
Go to DF and print registers there
Monitor441->